## Slide 1: Injector Status [Positron Source Upgrade]
KEKB injector linac
Takuya Kamitani
Belle2 GM (2014.06.18)

## Slide 2: SuperKEKB Injector
4.0 GeV e+
4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
RF gun
SuperKEKB injector
e+ target &
LAS capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER
AR
6.5 GeV e-
3T
RF gun
Damping ring for lower emittance (2000 -> 92[H]/7[V] mm)
Capture section upgrade for higher intensity (1 -> 4 nC)
  flux concentrator (e+ focusing pulsed solenoid)
  LAS [Large Aperture S-band accelerating structure]
Key issues in Positron Source Upgrade

## Slide 3: SuperKEKB positron station
positron
production
Target
Flux
Concentrator
Bridge
Coils
primary
e- beam
e+ beam
flux concentrator
target

## Slide 4: e+/e- beam switching & target hole
Flux
Concentrator
e+
injection e-
primary e-
bridge coils
target
beam
hole
pulse ST
DC QM
pulse QM
side view
rear view
injection e- beam ON-axis for low emittance preservation
target
offset
3.5 mm
2.0 mm
FC offset
7.0 mm
FC aperture
spoiler
target
diameter
4.0 mm
hole
diameter
2.0 mm
solenoid
Accel.
structure
primary e- beam OFF-axis with positron yield degradation

## Slide 5: Positron production target
target material selection
  high Z material
  high melting point
  high tensile strength
=> tungsten 14 mm long = 4.0 X0 4 mm diameter
beam hole for injection e-
tungsten
target
beam
hole
cooling water
pipe
primary
e- beam

## Slide 6: Beam spoiler for target protection
screen & scatterer
target
hole
injection
e- beam
primary e-
e+
hole
spot size
camera
beam spoiler to enlarge beam spot on target to be sx ,sy> 0.7 mm to avoid target destruction
spot size monitoring screen Al2O3 (0.14 mm thick) + scattering Al foil (0.25 mm thick) [total material thickness = 0.05 X0]
beam hole for injection e-
3m distance
Front
Rear

## Slide 7: flux concentration concept
DC current in primary coil produce uniform solenoidal field
Pulsed current & Conductor with slit => eddy current flows inner surface to generate high magnetic flux density (flux concentration !)
primary coil
conductor
conductor
primary coil
primary coil
but with non-axial symmetric transverse field !
=> transverse kick to positrons ! beam loss !

## Slide 8: e+ yield degradation by target offset
e+ yield degrades ~50 % by offset e+ generation
it can be improved to 78 % by
  utilizing transverse kick by proper orientation of FC slit
  e- incident position optimization
Bx
Bx-max = 0.15 T @ 12 kA
FC field map (Bx)
target
center
position

## Slide 9: Positron Capture Section
KLY
1-5
KLY
1-6
SLED
SLED
LAS 14 MV/m
deceleration & phase slip & acceleration
LAS 10 MV/m
acceleration
Solenoids
target
+FC
LAS : Large Aperture S-band structure
LAS
accelerating
structure
DC solenoid

## Slide 10: positron capture animation
Acceleration capture
Deceleration capture
Positrons with deceleration capture
favored for less halo and satellites !
from target to capture section exit (120 MeV)
Energy (MeV)
Energy (MeV)
longitudinal position (mm)
longitudinal position (mm)
You are watching longitudinal particle motion
(z-position vs energy) in a moving frame
riding on a microwave !

## Slide 11: e+/e- separator chicane
both secondary e+/e- are captured
to avoid disturbance of beam position monitors by mixture of e+/e- signals, only secondary e- are absorbed
pure e+ beam is transmitted
e- stopper block

## Slide 12: The first positron beam after the upgrade
BPM: SP_15_T in front of target
negative charged particles (e- beam)
give (-)(+) bipolar signal
BPM: SP_16_5 after e+ capture section
positive charged particles (e+ beam)
give (+)(-) signal
positron signal !!

## Slide 13: observed positron intensity
Gun
J-arc
target
Sector-2 end
Positron intensity
at positron line end
Q(e+) = 0.02 nC
Primary Electron
intensity at target
Q(e-) = 0.500 nC
orbit-X
[mm]
orbit-Y
[mm]
beam
intensity
[nC]

## Slide 14: Summary
Positron source components have been installed in the beam line (a target, a beam spoiler, a flux concentrator, bridge coils, DC solenoids, LAS accelerating structures, e+/e- separator chicane, plenty of quads)
Still in low spec. operation due to various constraints
  design full spec. achieved
  flux concentrator 12 kA 6 kA
  bridge coils 750 A 600 A
  DC solenoids 650 A 370 A
  LAS field gradient 14, 10 MV/m 10, 7 MV/m
We have observed the first positron beam after the upgrade ! (Qe+ = 0.02 nC @sector-2 end for Qe- = 0.5 nC @target) (Qe+ = 4 nC @sector-2 end for Qe- = 10 nC @target)
2014.06.09
SuperKEKB full spec.
x20
x200