## Slide 1: Electron/Positron Injector Phase-2 Status and Phase-3 Plan
Kazuro Furukawa
for Injector Linac, KEK

## Slide 2: Mission of Electron/positron Injector in SuperKEKB
  For 40-times higher luminosity in SuperKEKB collider
  Low emittance & low energy spread injection beams with 4 times higher beam current
    New high-current photo-cathode RF gun
    New positron capture section
    Positron damping ring injection/extraction
    Optimized beam optics and correction
    Precise beam orbit control with long-baseline alignment
    Simultaneous top-up injection to DR/HER/LER/PF/PFAR
  Balanced injection for the both photon science and elementary particle physics experiments
Injector Linac Mission
The single injector would behave as multiple injectors to multiple storage rings by the concept of virtual accelerator
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: Injector Linac Operation in Phase II - III
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
deceleration
positron target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
the same energy
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 4 GeV e+
beam injection with pulse-to-pulse variable charge and energy
device parameter change at 50 Hz (20 ms)
Pulsed magnet commissioning at 3-5 sectors (2017 autumn), and many more installation (2018-2019)
DC magnets
pulsed magnets
10 nC x 2 bunches x 50 Hz (LER)
4 nC x 2 bunches x 50 Hz (HER)
0.3 nC x 1 bunch x 25 Hz (PF-AR)
0.3 nC x 1 bunch x 25 Hz (PF)
variable energy pulse-to-pulse
beam bunches from e- gun

## Slide 4: Required injector beam parameters
Stage | KEKB (final) |  | Phase-I |  | Phase-II |  | SuperKEKB (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1 A | 1 A | – | – | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | 6 | 6
Bunch charge (nC) | primary e- 10 → 1 | 1 | primary e- 8 → 0.4 | 1 | 0.5 | 1 | primary e- 10 → 4 | 4
Norm. Emittance (ge) (mrad) | 1400 | 310 | 1000 | 130 | 200/40 (Hor./Ver.) | 150 | 100/15 (Hor./Ver.) | 40/20 (Hor./Ver.)
Energy spread | 0.125% | 0.125% | 0.5% | 0.5% | 0.16% | 0.1% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Eventually |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 
Linac Beam Property Requirements

## Slide 5
Phase II Operation
Summer Shutdown
Autumn Operation
Phase III
Summary

## Slide 6: Phase II Operation
Injector operation: Jan.12 – Jul.17
Proper SuperKEKB injection
Light source injection
  3 injections a day, top-up injection for hybrid mode PF experiments
  5-GeV PF-AR injection test
Stable operation of 64 new pulsed magnets at 50 Hz
4-beam simultaneous operation with thermionic gun
HER injection from RF-gun with slower beam switching
LER positron injection via damping ring
  with adequate timing and bucket selection
Instrumentation improvements
  Beam position monitors, profile monitors, bunch monitors
  Microwave monitors

## Slide 7: Pulsed Magnets
Pulsed quad x28 and pulsed corrector x 36 were newly commissioned on new girders (2017 autumn)
Good power supply stability of 0.01% (24 hours)
PXI bus, PXI-EVR, cRIO, 50 Hz controls with Windows and LabVIEW
More pulsed magnet commissioning expected (2018-2019)
Girder mover commissioning (1 micron alignment enabled, 2018-)
  Emittance brow-up investigations and mitigations
DC Quads
Pulsed Quads
Pulsed Correctors

## Slide 8: New Pulsed Magnets Enabled Simultaneous Injections
Horizontal
Vertical
Charge/bunch
HER
LER
PF
PF-AR
Stable Operation

## Slide 9: RF gun
Three Yb:YAG fiber oscillators
Redundant Yb:YAG fiber and Nd:YAG disk hybrid laser amplifiers
Dual laser injection on to IrCe cathode
Bunch current up to 3.6 nC
  2.4 nC at the end of linac (Phase II requirement: 1 nC)
2.4 nC
1st and 2nd laser together
1.5 nC
2nd laser only
3.6 nC
X (mm)
y (mm)
Q (nC)
X (mm)
y (mm)
Q (nC)

## Slide 10: HER Injection with RF Gun
RF-gun
Thermionic gun
・Safety system required 30 seconds to switch between guns before summer.

## Slide 11: Requirement for SuperKEKB
4 GeV
SuperKEKB5LER
7 GeV
SuperKEKB5HER
e-
Sector2
Sector3
Sector4
Sector5
Sector1
SectorA
SectorB
SectorC
Beam Transport lines (BT)
Jarc
After the LINAC, beam go through BT.
In Phase5III final, requirement of beam charge is 4 nC for both beam.
Requirement for H/V emittance of e+ beam is 100/15 μm.
Requirement for H/V emittance of e- beam is 40/20 μm.
We have to realize the high quality beam transportation to main ring without emittance growth as far as possible.
Otherwise, injection rate is worse and luminosity can not
reach the target value.
Electron gun
DR (damping ring)
Positron generation target
BT (Beam Transport line)
ARC (Bending section)
e+
Schematic layout of LINAC and beam transport line (BT)
Stage | Phase II (Mar. − Jul. 2018) |  | Phase III (Mar. 2019 −) | 
Beam | e+ | e– | e+ | e–
Bunch charge (nC) | 1.5 | 1 | 4 | 4
Norm. Emit. μm | 200/40 (Hor./Ver.) | 150 | 100/15 (Hor./Ver.) | 40/20 (Hor./Ver.)
Energy spread | 0.16% | 0.1% | 0.16% | 0.07%

## Slide 12: Injection Beam at KEKB and SuperKEKB
Comparison between achievement at KEKB and requirement at SuperKEKB Phase III
  Much smaller emittance even with 3-fold higher beam charge
  Still a big challenge that is being resolved
Charge (nC)
Norm. Hor.
Emit. (μm)
5
4
3
2
1
0
400
300
200
100
0
0.08
0.06
0.04
0.02
0
σδ(%)
1/7
1.3 times
400
300
200
100
0
Norm. Ver.
Emit. (μm)
1/15
3 times | 

## Slide 13: Residual Dispersion Function in Linac
Design
Before
After
Measured
Measured
Dispersion correction
Large residual dispersion was generated from the J–ARC.
With dispersion correction by tuning the magnetic field of quadrupole magnets, residual dispersion became small enough.
Y. Seimiya et al.

## Slide 14: Residual Dispersion Function in DR RTL
Example: 1st ARC
Extraction Kicker Extraction Septum
DC Bends
Need more study Before
After dispersion correction
Instead of changing the energy of DR, I changed the strength of Bend, Quad all at once. For the kicker and septum, Response measurement was done.
Optics of the extraction line
Y. Seimiya et al.
This table shows values of residual dispersion before and after correction.
Residual dispersion became smaller in both ARCs.
In 1st ARC, residual dispersion is not still small enough.
There are two ARCs in the DR extraction line.
The third graph shows residual dispersion. Blue is horizontal and red is vertical.
e+ | <ηx2>1/2 [m] |  | <ηy2>1/2 [m] |  | Fudge Factor of Quad.
Correction | Before | After | Before | After | [%]
2nd ARC | 0.079 | 0.019 | 0.0094 | 0.0077 | C 4.5
1st ARC | 1.05 | 0.09 | 0.02 | 0.01 | C 8.2

## Slide 15
Phase II Operation
Summer Shutdown
Autumn Operation
Phase III
Summary

## Slide 16: Summer Maintenance and Improvements
105 items were performed
From July 17th to October 22th
There were several near misses (no injuries)
  Taking measures against them
Morning meetings every day

## Slide 17
RF System Upgrade
Replacement of SHB1 Solid-State 10kW Amp.
20 years old, often unstable, degraded power
KL_13 Reinstallation
Solid-State Sub-Booster System
Replaced single 60-kW klystron with distributed 600W Solid-State Amplifiers
RF Monitor Upgrade (Pulse-Shortening Detector)

## Slide 18: Accelerating Units and Target Hole
Restoration of Unit 1-3
Replacement of markedly deteriorate accelerating structures in Units 1-1 and 5-1 with spares capable of rated power operation
Installation and adjustment of the power supplies for pulse magnets newly installed
Removal of the used FC base-unit and installation of the dummy plunger with holes for beam jitter measurement
Upgrade of control system for bending and solenoidal magnets
Restored Unit 1-3
Dummy plunger with holes (replacing target)

## Slide 19: Magnets and Beamline
Pulse magnets installed in beam-merger line of two pre-injectors. (bends x2, quads x4, correctors x4)
Corrector magnets added. (PY_12_2 [pulsed], BX_DS_C2 [DC])
DC corrector magnets removed in Sector-3, 4, 5. (pulsed correctors installed in summer 2017 summer)
Interlock system configuration improved. (e+ focusing DC solenoids, beam dump line quads)
Alignment of all beam-line girders and quads measured. Those with large deviation adjusted.
Remote control system installed in e+/e- beam separator.

## Slide 20: Development of New Beam Monitors
A new beam profile monitor with OTR target and high-precision optical focus system was installed at SY2 straight line. The resolution is expected to be 8 micron in FWHM.
A new beam timing monitor with stripline electrodes was installed at #A44. The resolution is expected to be 2 ps in RMS. Beam induced RF monitors are improved to held each other.

## Slide 21: Planning Pulsed Magnets for Merger Line
HER
LER (primary e– for e+）
PF-AR
PF
Thermionic Gun
Photo RF Gun
24-degree Merger Bend x2

## Slide 22: Pulsed Magnets for Merger Line

## Slide 23
Phase II Operation
Summer Shutdown
Autumn Operation
Phase III
Summary

## Slide 24: Injector Operation in Autumn 2018
Top-up injections to light sources, PF/PF-AR
  With pulsed magnets at beamline merger of guns
No positron damping ring operation
  Opportunity to study beam behavior at target hole
25 Hz mostly, followed by 3-day 50-Hz hardware checks
  First intense 50-Hz operation since 2011 earthquake in 2019
Emittance brow-up studies and knowledge acquisition
  Beam studies are planned, partially with simultaneous injection
Emittance preservation
  Beam orbit, optics controls and mover application
Gradual beam current and gradient improvements
  For later injection improvement

## Slide 25: Beam Phase Space Jitter
1nC
Linac end:
28 μm
7 μm
Linac end:
1.8 μm
0.9 μm
J-ARC e+ target
J-ARC e+ target
Before dispersion correction
After dispersion correction
First figure shows the standard deviation of beam position. Second figure shows emittance growth induced by beam jitter.
Beam phase space jitter is reduced by dispersion correction.
Small emittance growth still occurred from after the target after the correction.
We should understand the source of the beam jitter to prepare for the high charged beam (4 nC) and for accidental jitter source which occur at upstream the target.

## Slide 26: Emittance Growth at Target Hole (?)
In order to reveal beam jitter problem, simulation analysis of the wakefield in the target hole was performed.
Color variation shows difference of beam position from the center of target hole.
Wake potential in the target hole.
Longitudinal wake
Transverse wake
X = Beam position from the center of target hole.
Enlarged coefficient of beam position jitter:
~ 0.1@1nC << Measured enlarged coefficient
e+ e-
e-
φ2 mm
Y. Seimiya et al.

## Slide 27: Target Hole Study
Y. Enomoto et al.
To reveal beam jitter source directly, we temporally replace the target to dummy target with several hole, which have different diameter.
In this autumn, we will study the target hole effect on beam jitter.

## Slide 28: Simulation for Minimizing Emittance Growth Induced by Wakefield in Acceleration Structure
Phase;III requirement:
Horizontal : -
Vertical : -
( <50 μm)
( <20 μm)
LINAC end: γβεX:240 μm γβεY:120 μm
LINAC end: γβεX: 22 μm γβεY: 11 μm
s (m)
s (m)
End of LINAC
After orbit displacement is minimized
After emittance is minimized at the end of LINAC
Particle tracking simulation was performed to evaluate this emittance growth.
Simulation conditions:
Measured misalignments of acc. structure and quadrupole magnet were used.
Iris diameter of acc. structure is about 20 mm.
• εinj = 10 μm
• σz = 1.3 mm
• σδ = 0.4%
• Q = 5 nC
By the orbit correction for minimizing emittance growth, requirement of Phase III can be satisfied.
Blue and red dot show horizontal and vertical emittance, respectively.
Blue and red line shows horizontal and vertical requirement of Phase III.

## Slide 29
Phase II Operation
Summer Shutdown
Autumn Operation
Phase III
Summary

## Slide 30: Linac Schedule Overview as of Jun.2018
RF-Gun e- beam
commissioning
at A,B-sector
e- commiss.
at A,B,R,C,1
e+ commiss.
at 1,2 sector (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 sector
non damped e+ commiss.
at 1,2, 3,4,5 sectors
e- commiss. at A→5 sectors
damped e+ commiss.
at 1→5 Qe+ = 1~4nC
e- commiss.
at A→5 Qe- = 1~4nC
: Electron
: Positron
: Low current electron
1 - 2 nC
Phase2
1 nC
Phase1
Location
↓
Time →
Phase1: high emittance beam for vacuum scrub
Phase2,3: low emittance beam for collision
Schedule
Without Top-up
1 - 4 nC
Phase3
Improved RF gun
Direct PF-AR BT
DR Commiss.
Beam Licenses in steps
Low Emittance Beams
4+1 Ring
Injections
Low Emittance Injections

## Slide 31: For Phase 3
Simultaneous injections with some more pulsed magnets, in order to adjust beam optics and orbits
Some more beam instrumentation improvements
Positron target / flux concentrator restoration
50 Hz operation
Further instability hunt
Low emittance beam developments
Reliability, reproducibility, automation, etc.

## Slide 32: Summary
The injector performed Phase-2 commissioning without much troubles
The facility is believed to be ready for the first year in Phase-3, while it may face challenges to achieve the final beam qualities

## Slide 33: Thank you

## Slide 34: Injector Linac Overview
Injector linac configuration
  Major upgrade items
    Photo-cathode RF-gun for low-emittance e-
    Flux concentrator, LAS structure, solenoids, quads for e+
    Pulsed magnets for adequate beam optics for each beam
    High-precision beam position monitor
    High-precision beamline alignment for low emittance

## Slide 35: 概要 (2)
陽電子DR運転
  バケットセレクション，入出射タイミング
  低エミッタンス (垂直方向は良い．水平方向は悪い．BTで悪化する)
モニタ
  BPM: VMEデータ収集系
  A1ストリークカメラを3セクタ (34ユニット) に移設した．
  プロファイルモニタ:
    YAG:Ce, OTR (SC_34_2, SC_D4_4)
  RFモニタの活用
1. 入射器Phase II運転

## Slide 36: Simultaneous Injection (Thermionic Gun)
Stable Operation
Horizontal
Vertical
Charge/bunch
Horizontal
Vertical
Charge/bunch
HER
LER
PF
PF-AR

## Slide 37
Emittance improvement by dispersion correction
e+
0.7 [nC]
Horizontal Dispersion at Straight section after the Arcs
DR design emittance
Before Correction
After Correction in 2nd arc
After Correction in 1st arc
Fudge Factor of Quads [%]
<!x2>1/2 [m]
0.079
0.019
G 4.5
1.05
0.09
G 8.2
Measured Emittance in Sector 3
γβεx [μm]
293+44.5 192+22.4
1.84+0.163 2.01+0.363
126+8.2
64.3
γβεy [μm]
1.5+0.1
Thought the horizontal emittance became less than half, it is still twice as large as that of DR design.
Ms. Iida will talk this issue at the end of this session (TUPAB07).
A Residual dispersion in the DR extraction line (2)
Emittance was measured by wire scanner.
First, we corrected 2nd ARC dispersion. By the correction, emittance was improved from about 300 to 200.
Then, we corrected 1 ARC dispersion. By the correction,
st
emittance was improved to about 130.
Y. Seimiya et al.

## Slide 38: A) Residual dispersion in BT
Y. Seimiya,
N. Iida, M. Kikuchi
e+
<!x2>1/2 [m] <!y2>1/2 [m]
Fudge Factor of Quadrupole
Correction
Before After Before
0.27 0.02 0.01
0.037 0.047 0.126
- - -
- - -
- - -
- - -
After
[%]
BTp 0th ARC
0.03
-26-12.9
BTp 1st ARC
0.102
2.5
Slope 1
-
-
BTp 2nd, 3rd ARC
-
-
Slope 2
-
-
BTp 4th ARC
-
-
e;
<!x2>1/2 [m] <!y2>1/2 [m]
Fudge Factor of Quadrupole
Correction
Before After Before
0.13 0.11 0.05
0.11 0.02 0.01
0.102 0.038 0.029
0.066 0.029 0.037
0.104 0.091 0.192
- - -
After
[%]
Slope 1
0.01
1.0-5.9
Bte 0th ARC
0.02
0-6.7
Bte 1st ARC
0.036
2.37
Bte 2nd, 3rd ARC
0.034
2.52
Slope 2
0.116
3.55
correction for e- and Bte 4th ARC
-
-
BT-WS placed
BT-WS placed
Until BT-Wire Scanner (WS) position, dispersion correction was done.
In some ARC, dispersion correction is not finished. → Continue to Phase-III
Inj. point to MR
Inj. point to MR
As a same manner, we corrected dispersion in each ARC of BT.
This table shows residual dispersion before and after
e+ beam.
These ARC names are listed from the upstream of the beam line.

## Slide 39: B) Beam Phase Space Jitter (2)
First, we suspected that components around the target made beam jitter.
They are flux concentrator, solenoid, bridge coil, pulsed magnet, chicane, and so on.
We check whether these components are sources of jitter or not by turn off these components.
There is not remarkable differences.
The components are not the beam jitter source.

## Slide 40
D) Emittance growth induced by radiation excitation in BT
Theoretical emittance growth induced by radiation excitation:
∝ !5, 1/$3
Particle tracking simulation was performed from the end of LINAC to the end of BT.
Initial horizontal emittance of e8 and e+ beam have 20 and 64 µm, respectively.
These emittances are increased by radiation excitation and reach 68 and 74 µm.
Even if the emittance preservation is perfect in the LINAC, emittance growth by radiation
excitation is larger than Phase8III final requirement for the e8 beam.
We seek a solution of this problem now. One possible way is that other tunnel (AR line) is used as
e8 beam line, which has smaller ρ than that of current beam line.
N. Iida | Initial particles |  | With Radiation | Phase2III3final requirement
 | e8 (7 GeV) !" x [µm] | 20 | 68 | 40
 | e+ (4 GeV) !" x [µm] | 64 | 74 | 100

## Slide 41: Emittance measurement (e.)
N. Iida
Left and right figure show horizontal and vertical emittance measured at each sector, respectively.
Green and blue plot show emittance of beam generated by RF gun.
Manual orbit correction was done so as to reduce the orbit distortion. By this correction,
emittance was reduced.
In Phase.II, the requirement of e. emittance at the end of LINAC was satisfied.
However, emittance was increased in BT though dispersion correction was done.
This growth is not caused by radiation excitation because BT.WS is placed around the start of BT.
X
Y
1.2nC
Phase.III
Phase.III
Phase.II
Phase.II
reduced by orbit correction
5 BT
B C
5 BT
B C

## Slide 42: Emittance measurement (e+)
In Phase3II, the requirement of e+ emittance at the end of LINAC was also satisfied.
However, e+ emittance was also increased in BT though dispersion correction was done.
Investigations for this emittance growth source in BT are under going.
0.7nC
Y
B C
5 BT
B C
5 BT
X
Phase3II
Phase3III
Phase3III
Phase3II
N. Iida

## Slide 43: エミッタンス (mm∙mrad) バンチ電荷量: ～ 1 nC
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
陽電子 ex/ey ～200/2
電子 ex,y ～20
電子 ex,y ～ 40
BTにおけるエミッタンス増大(電子，陽電子)： ～ 200
1. 入射器Phase II運転
Phase II 目標値
電子: ex,y ～150
陽電子: ex / ey ～200 / 40
陽電子 ex/ey ～100/2

## Slide 44: Klystron Modulator Installation and Temporary Gun Removal
KL_DS/BCS
KL_DN/ECS
KL_32
 | ECS | BCS
Voltage required [MV] | 41 | 21.5
# 2m accelerator structure | 2 | 1
Accelerator field [MV/m] | 10.2 | 10.75
Operation power [MW] | 29.0 | 19.0
Pulse width [µs] | 0.8 | 0.8
Rep. rate [Hz] | 50 | 50
Other Improvements

## Slide 45: Newly Installed Pulsed Magnets
A | B | C | 1 | 2 | 3 | 4 | 5
Beam energy
Sector
Positron common optics
with some steering magnets
Independent beam optics
with pulsed magnets
HER (7 GeV)
LER (4 GeV)
PF-AR (6.5 GeV)
PF (2.5 GeV)
Independent beam optics with
26 Quads and 26 Correctors
in Sectors 3 – 5
10 Correctors in Sectors 1 and 2
2 Quads for Positron Target
Common optics was enough
KEKB
SuperKEKB

## Slide 46: Pulsed Magnet Installation 1
Installation during long shutdown at summer 2017
  Not possible before Phase 1 without DR because of the aperture
  Replacement for 64 magnets
  In 99 days between May and October
  All components including magnets, girders, cabling, cooling water, controls, etc.
  In parallel with other replacements and installations
2017/3/31 by N.Toge

## Slide 47: Pulsed Magnet Installation 2
13 New girders
  each for 2 quads and 2 correctors
  ready for 10 μm alignment to realize low emittance preservation in Phase 3

## Slide 48: Pulsed Magnet Installation 3
Standard cabinet configuration for pulsed magnets
4 quads and 4 correctors for a half sector
Controls
Pulsed power supplies & Interlock system
for 2 quads and 2 correctors
Pulsed power supplies & Interlock system
for 2 quads and 2 correctors
Girder and magnet replacements before July
Power supply installation and cabling before September
Comprehensive system tests in September for a month

## Slide 49: Performance of Quad Power Supply
High performance with energy recovery
  Total energy recovery rate of 68.5％ (measured)
  No need for additional wall power (only 39kW for all new magnets)
High precision and high stability by analog feedback with IGBT
  Stability of 0.01％ for 24 hours
Flexible synchronous controls with global event control system
  Independent pulse-by-pulse modulation at 50 Hz
Drives a 1 mH coil at 330 A, 340 V, 1.5 ms risetime

## Slide 50: Power Consumption Measurement
Chart: Quad (50 Hz, 300 A) x 1
| Pjoule-mag | Pjoule-cable | PL | Ptotal | Pmeasured
Q (50 Hz, 300 A) x 1 | 76 | 302.6 | 2250 | 2628.6 | 827
Energy stored in coil inductance
Heat loss on cables
Heat loss at Magnet
Total Energy
Actual power consumption (measured)
Energy recovery ratio = 1 - Pmeasured / Ptotal = 68.5 %

## Slide 51: Stability of Quad Power Supply
0.014578 A / 165.946 A = 0.0107% / 24 hours (for PF_52_4 magnet)
25 mA / div

## Slide 52: Examples of Other Recent Improvements
Energy and bunch compressors on the beam transport of DR
Beam lines and power supply rearrangement for DR BT
Thermionic gun and bunchers
Beam position monitors
Wire scanners and streak cameras
LLRF system to co-op with event timing controls
LLRF monitors
Independent RF amplifiers
Alignment
Direct beam transport to PF-AR
Safety system and radiation control licenses
Rejuvenation of old components
Operation software
Operation manuals
Other Improvements