## Slide 1: Injector LINAC Status
  Kazuro Furukawa for Injector LINAC
  <http://www-linac.kek.jp/linac-paper/general/>
  Information from all injector group members

## Slide 2: Improved Precision/Flexibility Injections
    HER: 800mA, 12.5 – 25 Hz,
    1.4 nC, 1 bunch LER: 1000mA, 12.5 – 25 Hz, 3.0 nC, 1-2 bunch
    PF ring: 450mA, <1 Hz,
    0.25 nC
    PF-AR: 50mA, <1 Hz,
    0.3 nC
  Typical 1-day Injections
Four virtual injectors have enabled high efficiency simultaneous top-up injections
The injector provide high availability with advanced high-current and low-emittance injections for SuperKEKB as well as light source rings
(Achieved 200 thousand hours of operation at the middle of 2020)
  red: Ring current (mA)
  blue: Bunch charge (nC)
  green: Injection rate (mA/s)

## Slide 3: Recent LINAC Development and Progress
Flux
Concentrator
e+
injection e-
10 nC
primary e-
bridge coils
target
beam
hole
pulsed corr.
DC quad
pulsed quad
top view
spoiler
solenoid
LAS Accel.
structure
New accelerating structures were designed and are being fabricated
Planning to replace damaged 40 year-old 7% in 230 accelerating structures
Succeeded to achieve high acceleration field and low discharge rate with the first 4 structures
Will install 12 more structures in 2023
Can reach Υ (6S)
  Steady progress of positron beam
  Flux concentrator
  Present operation
  Operation up to the last year
  Design to achieve high performance
  4 new structures installed
Positron production yield reaching designed value
Copper-Nickel alloy was applied to flux-concentrator and resolved the discharge issues
Optimized with newly installed correctors and monitors
3 nC/bunch enough for present SuperKEKB operation
  Positron yield
H. Ego
Y. Enomoto

## Slide 4: Electron Beam from RF gun
Beam emittance
  Present requirement γεx 100 μm, γεy 40 μm
  Stability improvements
    DOE for 2nd laser
    Stabilization closed loops
    7 additional pulsed correctors
  Emittance blow-up in later part of BT
    Needs further studies
    CSR is suspected
      Vertical blow-up ?
      Blow-up behavior with modified optics condition ?
    Orbit stability
      To avoid sextupole field fluctuation from bends
      Mitigation by permanent magnet sextupole correctors
At 1.5 GeV
1st half of BT

## Slide 5
by*=8mm
by*=1mm
Energy scan
Injection study
HER “raw” injection efficiency reached 80-90 % !
③Dec.1, Septum
Angle: 2.6→2.5
②Nov.18, Septum
Angle:2.57→2.68
①Nov.9 Optics
matching BTe1
④Nov.18 Energy adjusted
with TbT-BPM
Injection-1. Improvement of HER injection
HER injection for by*=1mm has improved, achieved from 60% to 80%.
N. Iida

## Slide 6
2.85
2.96
3.5
Injection-2. Understanding the injection orbit
M. Kikuchi, Feb.4
  The horizontal orbit of the injection beam for HER has little room to the wall of the injection point chamber.
  Fairly high residual radioactivity here is observed.
  It is planned that this chamber will be replaced with a wider one during LS1.

## Slide 7
Smaller fluctuation of the X of the “Inj-BPM” is better.
“raw” efficiency
X inj-BPM
“raw” efficiency
X inj-BPM
HER
Nov.18
Injection-3. “Injection-BPM” became a good reference
The horizontal position at “Injection-BPM”, so-called “Mitsuka-monitor”, has a correlation with the ”raw” injection efficiency.
Septum angle was tuned so as to increase the charge at “Inj-BPM”.
Charge at “Inj-BPM”
Septum angle:
2.55→2.68
G. Mitsuka, T. Mori, Y. Ohnishi, S. Ogasawara, N. Iida
  The injection tuning panel for the septum magnets has been redesigned considering the design orbit that reduced beam losses at the injection point.
  The signal of the special beam position monitor (“Injection-BPM”) for the injected beam became clear, which helped the injection tuning so much.

## Slide 8
OTR
OTR
WS
OTR
WS
WS
OTR
WS measurements may includes beam jitters.
Injection-4. Emittance blowup in the BT lines
Positron
Electron
Horizontal
Vertical
The emittance blowups between BT1 and BT2 are still unresolved.
  The horizontal emittance blowup is now observed not only in e- BT but also in e+ BT by increasing beam charge.
  A coherent synchrotron radiation (CSR) is now the most suspected.
  We are investigating whether the emittance blowup has charge dependence.
N. Iida

## Slide 9: Injector Linac Improvements
Short term：Summer 2021
  Optical element and amplifier for 2nd Laser of Rf-gun
  Photo cathode and laser window replacement
  Core/Edge network switch upgrade
  7 pulsed corrector magnet addition
  Solid-state amplifiers replacing mid-power klystron
  Damaged waveguide renewal
  Beam position monitor just after positron target
  Improved secondary RF-gun as backup
  Improved protection against AC 50Hz fluctuation
Mid-term：up to 2026
  Pulsed magnets & kicker
  Precision girder mover
  Energy compression system
  Improved RF-gun
  Improved positron generation
  Accelerating structure upgrade
  PCB capacitor renewal
Energy compression
PCB capacitor renewal
High-precision mover
Pulsed magnets
Positron generation
RF gun
Accelerating structure
Laser stabilization with DOE element
Secondary RF-gun
Core network switches
New beam position monitor

## Slide 10
A
B
C
1
2
3
4
5
HER electron
7.0 GeV
4 nC x 2
LER positron
4.0 GeV
4 nC x 2
3.2 GeV, 10nC x 2
1.1 GeV positron damping ring
Energy compression
Bunch compression
PF ring
2.5 GeV
0.2 nC
RF gun with 4 nC
Positron generation
PF-AR
6.5 GeV
0.2 nC
J-arc
1.5 GeV
Energy compression
Thermionic gun with 10 nC
New energy compressor
PCB capacitor renewal
High precision movers
Pulsed magnets/kickers
Injector Linac Upgrade Items 2022 - 2026
Positron capture section
RF gun
Accelerating structure

## Slide 11: Pulsed Magnet, Kicker and Mover
Ceramics chamber integrated kicker development
Pulsed magnets and power supplies
High-precision girder movers
Injector linac injects beams into SuperKEKB HER, LER as well as light sources PF, PF-AR with adequate beam properties at 50 Hz maximum in simultaneous top-up injection scheme. Pulsed magnets, kicker magnets and girder movers will be installed in order to suppress emittance blow-up caused by wakefield in accelerator structure with 4 nC per bunch. Kicker magnets may correct beam orbits separated by only 96 ns. Girder movers may compensate 2-mm annual floor drift at less than 10 microns.
Y. Enomoto
Y. Enomoto, T. Natsui
C. Mitsuda

## Slide 12: Higher Energy Injection and Collision
Mitigation of accelerator structure issues
  Originally designed for 8 MeV/m, but has been used at 20 MeV/m
  Degradation that lead to high field emission rate and discharges
  Water leaks
  Not only Y(6S) but even Y(4S) could be endangered
4-year plan to fabricate and install new accelerator structures
  Demands for light source operation may delay the installation until summer 2023

## Slide 13: New Accelerating Structures and ECS for Electron Beam
回折光学素子による形状補正
7% of 230 accelerating structures will be replaced for mitigation of 40-years of degradation by discharges and water leaks.
電子銃空洞と光陰極
26m
H
E
E
H
E
H
E
H
H
E
E
E
E
10000
2000
2000
1000
1000
1000
1000
1000
1000
1000
1000
Energy compression system (ECS) for electron beam will be installed at the beginning of the beam transport line.
Additional replace-ment will be necessary in near future.

## Slide 14: Capacitors with PCB contamination
Capacitors (up to 1200) in power modulators with low-level PCB produced before 1991 will be replaced following the law.
Injector linac continues to improve with hardware upgrade in 7 category regions from 2022 to 2026.
Capacitors in high-power klystron modulators

## Slide 15: Further Injector Improvement Possibilities
After injector upgrade in 7 categories
  Difficult to foresee now which parameter to improve further
Under consideration
  Further increase in positron bunch charge
    LER stored current is higher and beam lifetime is shorter
    Several possible plans exist
  Beam transport line thru the direct tunnel
    May relax CSR, etc
    May interfere with PF-AR operation
  Even higher energy
    Not difficult in ring hardware up to 12 GeV with different energy ratio
    Collision optics design should be investigated
    Quite expensive modification at LINAC and beam transport line
  Polarization
    Physics demand
    R&D for resources, space, meaningful bunch charge
  …

## Slide 16: Positron Generation Improvements
Improvement at summer 2020
  Cu-Ni alloy for flux concentrator
  Routine 12 kA operation
  Correctors inside of 15-m solenoid section
  Accelerating structure & load
  Stable 3 nC positron delivery in 2021
Flux
Concentrator
e+
4 nC injection e-
10 nC
primary e-
bridge coils
target
beam
hole
pulsed corr.
DC quad
pulsed quad
top view
spoiler
solenoid
LAS Accel.
structure

## Slide 17: Further Positron Enhancement
Optimization of capturing and bunching
  Accelerating voltage gradually increasing
    Long-term RF conditioning
    Discharge in dummy loads and waveguides being resolved
  Several beam monitors and correctors were added
    Spiral beam orbit behavior in solenoid with large energy spread
    Normal bunching or velocity (decelerating) bunching
Time
Signal
Positron
Electron
New BPM that measures electron and positron separately just after the target before the electron separator. This helps understand positron behavior in solenoidal field.
Monitor head

## Slide 18: Further Positron Enhancement (II)
Successful resolution of discharge at flux concentrator
  Introduction of copper-nickel alloy
Successful mitigation of spike waveform
  Simulation of equivalent circuit with detailed stray capacitance
Higher current and higher magnetic field possibility
  With power modulator upgrade
Simulation with improved equivalent circuit and the new design
Actual application of the new design
T. Natsui

## Slide 19: Further Positron Enhancement (III)
Positron beam not at the center of solenoid / structure
  In order to pass electron beam at the center of structure with lower wakefield
  The target is 3.5 mm away from the center of structure and 1.5 mm away from the center of flux concentrator, responsible for spiral beam and lower mag field
Solenoidal field gap between flux concentrator and structure
  For maintainability at high radiation region
  After several years of experience, shorter gap possibility
Both are the sources of positron loss, and new design is underway
Rear view
Top view

## Slide 20: Carbon Neutral Activities at Injector LINAC
High Performance Simultaneous Top-up Injections
69% Power Recovery from Pulsed Magnet Coils
High Power Conversion Efficiency at Magnet Power Supplies
High Efficiency RF Power Distribution

## Slide 21: Responses to previous BPAC Comments
Although the current injection rate is adequate, improvements will be needed to achieve higher stored beam currents and shorter ring lifetime.
  Much improved with a new beam injection monitor. Several possible ideas are being investigated, including physical aperture, optics matching, magnetic field compensation, mitigation of CSR by new beam duct, more synchronized beam instrumentations, etc.
The positron yield is below the design value. The positron yield needs to be improved in order to keep up with the expected short lifetime of the LER as beam currents increase.
  Several possible scenarios were presented in this presentation. Presently, it is said to be large enough for the bucket charge quantization.
The HER injection rate also is low and there is still the emittance increase in the BT to the ring.
  We are slowly studying the beam behavior between collision operation.
Further studies on the two-bunch injection for the HER is encouraged, most likely requiring dedicated machine time.
  Thanks for the recommendation, we will balance it with collision operation and ring study.
The committee encourages expanding the effort to improve the modelling of the current BT in order to understand where the emittance blowup is occurring; e.g. how much a lattice error needs to be increased in order to induce the observed emittance blowup.
  We began to understand where the blowup starts, etc. with limited instrumentations.

## Slide 22: Summary
Injector LINAC continues reasonable injections in simultaneous top-up injection mode.
Emittance blow-up at the 2nd half of beam transport line is still under investigation, but is partially relaxed recently with finer parameter tuning to make injection and storage beams match.
The injector upgrade was discussed and will be implemented in 7 categories for the final beam parameters with higher bunch charges and lower transverse and longitudinal emittances. Further upgrade is also investigated.

## Slide 23: Thank you

## Slide 24
Backup

## Slide 26: DR Optics Change
H. Sugimoto
(A) Optics using the operation
(B) Low emittance optics
(Failed in Apr.2021)
(C) Half-low-emittance optics
(Feb.2022)

## Slide 27: Linac Beam Parameters for KEKB/SuperKEKB
Linac Beam Property Requirements
Gradual improvements keeping light source injections
Stage | KEKB (final) |  | Phase-I (achieved) |  | Phase-II (achieved) |  | Phase-III (interim) |  | Phase-III (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1.0 A | 1.0 A | – | – | 1.8 A | 1.3 A | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | – | – | 6 | 6
 | primary e- 10 |  | primary e- 8 | 1 | 0.5 | 1 | 2 | 2 | primary e- 10 | 4
Bunch charge (nC) | → 1 | 1 | → 0.4 |  |  |  |  |  | → 4 | 
Norm. Emittance | 1400 | 310 | 1000 | 130 | 200/40 | 150 | 150/30 | 100/40 | 100/15 | 40/20
(gbe) (mrad) |  |  |  |  | (Hor./Ver.) |  | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.)
Energy spread | 0.13% | 0.13% | 0.50% | 0.50% | 0.16% | 0.10% | 0.16% | 0.10% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Partially |  | 4+1 rings (LER, HER, DR, PF, PF-AR) |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 

## Slide 28: Emittance Preservation
Offset injection may solve the issue
Orbit have to be maintained precisely
Mis-alignment should be <0.1mm locally, <0.3mm globally
100 samples
Mis-alignment leads to Emittance blow-up
Sugimoto et al.
Orbit manipulation compensates it
Alignment

## Slide 29: Floor vertical movement in a half year from summer to winter
C3
11
18
28
38
48
Higo et al.
Alignment