## Slide 1: Electron/Positron Injector Phase-2 Status and Phase-3 Plan
Kazuro Furukawa
for Injector Linac, KEK

## Slide 2
Overview
Beam Quality Management
Accelerating Structure
Summary

## Slide 3: Mission of Electron/positron Injector in SuperKEKB
  For 40-times higher luminosity in SuperKEKB collider
  Low emittance & low energy spread injection beams with 4 times higher beam current
    New high-current photo-cathode RF gun
    New positron capture section
    Positron damping ring injection/extraction
    Optimized beam optics and correction
    Precise beam orbit control with long-baseline alignment
    Simultaneous top-up injection to DR/HER/LER/PF/PFAR
  Balanced injection for the both photon science and elementary particle physics experiments
Injector Linac Mission
The single injector would behave as multiple injectors to multiple storage rings by the concept of virtual accelerator
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 4: Injector Linac Operation in Phase II - III
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
deceleration
positron target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
the same energy
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 4 GeV e+
beam injection with pulse-to-pulse variable charge and energy
device parameter change at 50 Hz (20 ms)
Pulsed magnet commissioning at 3-5 sectors (2017 autumn), and many more installation (2018-2019)
DC magnets
pulsed magnets
10 nC x 2 bunches x 50 Hz (LER)
4 nC x 2 bunches x 50 Hz (HER)
0.3 nC x 1 bunch x 25 Hz (PF-AR)
0.3 nC x 1 bunch x 25 Hz (PF)
variable energy pulse-to-pulse
beam bunches from e- gun

## Slide 5: Required injector beam parameters
Linac Beam Property Requirements
Stage | KEKB (final) |  | Phase-I |  | Phase-II |  | Phase-III (2019) |  | Phase-III (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1.0 A | 1.0 A | – | – | 1.8 A | 1.3 A | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | – | – | 6 | 6
 | primary e- 10 |  | primary e- 8 | 1 | 0.5 | 1 | → 2 | → 2 | primary e- 10 | 4
Bunch charge (nC) | → 1 | 1 | → 0.4 |  |  |  |  |  | → 4 | 
Norm. Emittance | 1400 | 310 | 1000 | 130 | 200/40 | 150 | 100 | 40 | 100 / 15 | 40 / 20
(gbe) (mrad) |  |  |  |  | (Hor./Ver.) |  |  |  | (Hor./Ver.) | (Hor./Ver.)
Energy spread | 0.13% | 0.13% | 0.50% | 0.50% | 0.16% | 0.10% | 0.16% | 0.10% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings |  | No top-up |  | Partially |  | 4+1 rings |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 
 | (LER, HER, PF) |  |  |  |  |  |  |  |  | 

## Slide 6: Beam Commissioning Activities
  Low emittance electron High efficiency Beam control
  from RF gun positron capture with ~70 pulsed magnets
  Injection beam for SuperKEKB Emittance optimization
 | KEKB (− 2010) |  | SuperKEKB Phase III | 
Beam | e+ | e– | e+ | e–
Bunch charge (nC) | 1.0 | 1.0 | 4.0 | 4.0
Normalized Emittance (μm) | 1400 | 310 | 100/15 (Hor./Ver.) | 40/20 (Hor./Ver.)
Energy spread | 0.125% | 0.125% | 0.16% | 0.07%

## Slide 7: Injector FY2019 Plan
Realize stable and sufficient beams for the first year of Phase 3 commissioning
Perform 3-year program to recover degradation of accelerating structures
Postpone remaining upgrades until later years, limit backup devices, in order to support longer operation hours even under limited resources in FY2019

## Slide 8
Overview
Beam Quality Management
Accelerating Structure
Summary

## Slide 9: Injector Operation in Autumn 2018
Top-up injections to light sources, PF/PF-AR
  With pulsed magnets at beamline merger of guns
No positron damping ring operation
  Opportunity to study beam behavior at target hole
25 Hz mostly, followed by 3-day 50-Hz hardware checks
  First intense 50-Hz operation since 2011 earthquake in 2019
Emittance brow-up studies and knowledge acquisition
  Beam studies are planned, partially with simultaneous injection
Emittance preservation
  Beam orbit, optics controls and mover application
Gradual beam current and gradient improvements
  For later injection improvement

## Slide 10: Injection Beam at KEKB and SuperKEKB
Comparison between achievement at KEKB and requirement at SuperKEKB Phase III
  Much smaller emittance even with 3-fold higher beam charge
  Still a big challenge that is being resolved
Charge (nC)
Norm. Hor.
Emit. (μm)
5
4
3
2
1
0
400
300
200
100
0
0.08
0.06
0.04
0.02
0
σδ(%)
1/7
1.3 times
400
300
200
100
0
Norm. Ver.
Emit. (μm)
1/15
3 times | 

## Slide 11: Beam Quality
Beam emittance
Beam energy spread
Stabilities of beam position, energy, etc
Beam position jitter (painted jitter emittance)
Beam energy jitter (painted energy spread)
Degradation of above beam qualities can be the source of injection background
Hardware components and their monitor systems were much improved

## Slide 12
1nC
Linac end:
28 μm
7 μm
Linac end:
1.8 μm
0.9 μm
J-ARC e+ target
J-ARC e+ target
Before dispersion correction
After dispersion correction
The top plot shows the standard deviation of beam position. The middle plot shows emittance growth induced by beam jitter.
Beam phase space jitter is reduced by dispersion correction.
Small emittance growth still occurred from after the target after the correction.
We should understand the source of the beam jitter to prepare for the high charged beam (4 nC) and for accidental jitter source which occur at upstream the target.
Beam Phase Space Jitter Reduction
Seimiya et al.

## Slide 13: Residual Dispersion Function in Linac
Design
Before
After
Measured
Measured
Dispersion correction
Large residual dispersion was generated from the J–ARC.
With dispersion correction by tuning the magnetic field of quadrupole magnets, residual dispersion became small enough.
Y. Seimiya et al.

## Slide 14: Energy Stabilizer (Energy FB)
BT
The injection energies have been stabilized within ±0.03% by the energy feedback.
Target
Energy knob
Beam energy
( monitored)
±0.03%
Jarc
FB ON
FB ON
Iida et al.

## Slide 15: Energy jitter
Diamond became small
After suppressing the energy jitter,
the signal from Diamond detector was reduced.
Energy Jitter
±0.1%
±0.05%
CLAWS
Beam background is sensitive to the energy jitter.
Energy FB did not work well.
Iida et al.

## Slide 16: Emittance Growth at Target Hole (?)
In order to reveal beam jitter problem, simulation analysis of the wakefield in the target hole was performed.
Color variation shows difference of beam position from the center of target hole.
Wake potential in the target hole.
Longitudinal wake
Transverse wake
X = Beam position from the center of target hole.
Enlarged coefficient of beam position jitter:
~ 0.1@1nC << Measured enlarged coefficient
e+ e-
e-
φ2 mm
Y. Seimiya et al.

## Slide 17: Target Hole Study
Y. Enomoto et al.
To reveal beam jitter source directly, we temporally replace the target to dummy target with several hole, which have different diameter.
In this autumn, we will study the target hole effect on beam jitter.

## Slide 18: Jitter Emittance after Target
With Target hole(φ2mm)
No Target hole
The growth of the jitter emittance has been nothing to do with the small hole.
Strong correlation between orbit jitter and beta function.
The beta function after the target is large to squeeze the beam sizes to pass through the hole, which causes the large orbit jitter.
The result is;
Although the jitter emittances are still increased as shown in the jitter emittance plots, it is known that this jitter becomes smaller when Jarc's dispersion leakage is reduced.
They are small enough at the end of LINAC.
Position jitters x, y [mm]
√bx, √by

## Slide 19: Simulation for Minimizing Emittance Growth Induced by Wakefield in Acceleration Structure
Phase;III requirement:
Horizontal : -
Vertical : -
( <50 μm)
( <20 μm)
LINAC end: γβεX:240 μm γβεY:120 μm
LINAC end: γβεX: 22 μm γβεY: 11 μm
s (m)
s (m)
End of LINAC
After orbit displacement is minimized
After emittance is minimized at the end of LINAC
Particle tracking simulation was performed to evaluate this emittance growth.
Simulation conditions:
Measured misalignments of acc. structure and quadrupole magnet were used.
Iris diameter of acc. structure is about 20 mm.
• εinj = 10 μm
• σz = 1.3 mm
• σδ = 0.4%
• Q = 5 nC
By the orbit correction for minimizing emittance growth, requirement of Phase III can be satisfied.
Blue and red dot show horizontal and vertical emittance, respectively.
Blue and red line shows horizontal and vertical requirement of Phase III.

## Slide 20
Overview
Beam Quality Management
Accelerating Structure
Summary

## Slide 21: Injector Linac Beam Acceleration
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
deceleration
positron target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
the same energy
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 4 GeV e+
60 acceleration units are employed each with 4 acceleration structures.
Beams are accelerated/decelerated as well as energy/bunch-compressed with them.
DC magnets
pulsed magnets
10 nC x 2 bunches x 50 Hz (LER)
4 nC x 2 bunches x 50 Hz (HER)
0.3 nC x 1 bunch x 25 Hz (PF-AR)
0.3 nC x 1 bunch x 25 Hz (PF)
variable energy pulse-to-pulse
beam bunches from e- gun

## Slide 22
Designed performance of the accelerating unit
Klystron output
40 MW 4 us
SLED output
140 MW(mean) 0.5 us
Va = 160 MV (21 MV/m)
by four structures
Waveguides
~10% power loss
Acceleration Unit Configuration
Notes: This illustrates an S-band accelerating unit in the linac.
The output RF power of the klystron is compressed to approximately 140 MW through the SLED.
We divide the power into four and feed them into the four accelerating structures by using a vacuum waveguide circuit.
Then the unit generate an accelerating voltage of 160 MV.

## Slide 23
Three types of S-band quasi-constant-gradient accelerating structures of 2 m in length are employed
as main accelerators
PF-type accelerating structures 142 (19 + 6 units have issues)
KEKB-type accelerating structures 74
Large-aperture accelerating structures (LAS) * 10
* special structure for the positron capture unit
Type
Number in use
Accelerating Structures

## Slide 24
Not interchangeable
Complicated fabrication
Used at 8 MeV/m since 35 years ago
Later raised to 21 MeV/m
PF-type structure
KEKB-type structure
Revised structure
Designed for 21 MeV/m
Accelerating Structures

## Slide 25
PF-type structures
fabricated about 35 years ago as the injector for the PF ring
don’t work well
Mean RF parameters of five kinds of the PF-type | 
ra [MΩ/m] | 57.8 (57.3 - 58.3)
τ [neper] | 0.335 (0.302 - 0.368)
Tf [us] | 0.51 (0.462 - 0.558)
Va/P1/2 [MV/MW1/2] | 7.29 (7.00 - 7.58)

## Slide 26
KEKB-type structures
Mean RF parameters of five kinds of the KEK-type | 
ra [MΩ/m] | 57.8 (57.3 - 58.3)
τ [neper] | 0.335 (0.302 - 0.368)
Tf [us] | 0.51 (0.462 - 0.558)
Va/P1/2 [MV/MW1/2] | 7.29 (7.00 - 7.58)
fabricated about 20 years ago for the KEKB injector
work well as designed
the same as those of the PF-type

## Slide 27
Field emission, reflection (19)
Cooling water leakage (6)
water leak
Need interim fix with sealant
・Some of water leakage are fatal
・Approx. 3 leakages per year, in recent years
・May increase as they are built at a time
・Improving the identification of a damage in four structures
・No more healthy PF-type backup structures
・Have to utilize degraded structures in an emergency
not recoverable
Lower acceleration
Has to fix
Degradation of Acceleration Units

## Slide 28
M
C
ST
B
C
M
C
ST
C
B
T
F
C
M
C
ST
B
C
M
C
ST
C
B
T
F
C
Contract
Design
Materials
Coupler
Structure
#1, 2 Structures
#3, 4 Structures
FY20xx
FY20xx + 1
Fabrication schedule
M
C
ST
B
T
F
加工
検査と測定
表面処理
組立
性能調整
最終組立
As a solution, structures are newly designed with lower emission and higher gradient
・4 structures per year
・12 structures for 3 years
・Scheduling from FY2018-9 even under limited budget stopping other improvements
New Structure Production

## Slide 29
Overview
Beam Quality Management
Accelerating Structure
Summary

## Slide 30: Linac Schedule Overview
RF-Gun e- beam
commissioning
at A,B-sector
e- commiss.
at A,B,R,C,1
e+ commiss.
at 1,2 sector (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 sector
non damped e+ commiss.
at 1,2, 3,4,5 sectors
e- commiss. at A→5 sectors
damped e+ commiss.
at 1→5 Qe+ = 1~4nC
e- commiss.
at A→5 Qe- = 1~4nC
: Electron
: Positron
: Low current electron
1 - 2 nC
Phase2
1 nC
Phase1
Location
↓
Time →
Phase1: high emittance beam for vacuum scrub
Phase2,3: low emittance beam for collision
Schedule
Without Top-up
1 - 4 nC
Phase3
Improved RF gun
Direct PF-AR BT
DR Commiss.
Beam Licenses in steps
Low Emittance Beams
4+1 Ring
Injections
Low Emittance Injections

## Slide 31: For Phase 3
Positron target / flux concentrator restoration
50 Hz operation
Simultaneous injections for 4 storage rings with beam stabilization feedback loops
Further instability hunt
Low emittance beam developments
Reliability, reproducibility, automation, etc.

## Slide 32: Summary
The injector performed beam improvements after Phase-2 towards Phase-3 commissioning
The facility is believed to be ready for the first year in Phase-3, while it may face challenges to achieve the final beam qualities

## Slide 33: Thank you

## Slide 35: Lifetime and injection rate
Example : Phase 3-3ex Parameter
 | LER | 
Life time [sec.] | 600 | Nb=1578, Itot=2.0A
Loss Rate [mA/sec] | 3.0 | 
frev=100kHz
QBTend=1.0nC
frep=25Hz
nbunch=2
effinj=70%
Even if such a low charge injection, the total beam current can be kept
with 25Hz injection.
Assumed from the lifetime of Phase 2

## Slide 36: Nondestructive Energy Spread Monitor： eight electrode BPM in Jarc
The beam spread can be measured from the second moment.
Second moment and horizontal profile
F. Miyahara
sx monitored with
screen monitor
sx monitored with
OctoPos BPM
Although the profile with two peaks ② can not be recognized from ⑥ only with the second moment, it is important to keep the energy spread to ③ or ④.
①
②
③
④
⑤
⑦
⑥

## Slide 37: Other voltage fluctuation of klystron power supply
C1: RF voltage
C1: RF Phase
7deg
5%
RF voltage / phase variation
Klystron output power is stabilized by
Induced Voltage Regulator (IVR) at the sudden change of AC line voltage.
In Phase 2, IVR stabilization had been done once an hour.
It is planed to establish the IVR feedback in Phase 3.
Sometimes the AC line voltage for klystron power supply drops.
Beam energy stabilization

## Slide 38: Injector Linac Overview
Injector linac configuration
  Major upgrade items
    Photo-cathode RF-gun for low-emittance e-
    Flux concentrator, LAS structure, solenoids, quads for e+
    Pulsed magnets for adequate beam optics for each beam
    High-precision beam position monitor
    High-precision beamline alignment for low emittance

## Slide 39: Required injector beam parameters
Stage | KEKB (final) |  | Phase-I |  | Phase-II |  | SuperKEKB (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1 A | 1 A | – | – | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | 6 | 6
Bunch charge (nC) | primary e- 10 → 1 | 1 | primary e- 8 → 0.4 | 1 | 0.5 | 1 | primary e- 10 → 4 | 4
Norm. Emittance (ge) (mrad) | 1400 | 310 | 1000 | 130 | 200/40 (Hor./Ver.) | 150 | 100/15 (Hor./Ver.) | 40/20 (Hor./Ver.)
Energy spread | 0.125% | 0.125% | 0.5% | 0.5% | 0.16% | 0.1% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Eventually |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 
Linac Beam Property Requirements

## Slide 40
Emittance improvement by dispersion correction
e+
0.7 [nC]
Horizontal Dispersion at Straight section after the Arcs
DR design emittance
Before Correction
After Correction in 2nd arc
After Correction in 1st arc
Fudge Factor of Quads [%]
<!x2>1/2 [m]
0.079
0.019
G 4.5
1.05
0.09
G 8.2
Measured Emittance in Sector 3
γβεx [μm]
293+44.5 192+22.4
1.84+0.163 2.01+0.363
126+8.2
64.3
γβεy [μm]
1.5+0.1
Thought the horizontal emittance became less than half, it is still twice as large as that of DR design.
Ms. Iida will talk this issue at the end of this session (TUPAB07).
A Residual dispersion in the DR extraction line (2)
Emittance was measured by wire scanner.
First, we corrected 2nd ARC dispersion. By the correction, emittance was improved from about 300 to 200.
Then, we corrected 1 ARC dispersion. By the correction,
st
emittance was improved to about 130.
Y. Seimiya et al.

## Slide 41: A) Residual dispersion in BT
Y. Seimiya,
N. Iida, M. Kikuchi
e+
<!x2>1/2 [m] <!y2>1/2 [m]
Fudge Factor of Quadrupole
Correction
Before After Before
0.27 0.02 0.01
0.037 0.047 0.126
- - -
- - -
- - -
- - -
After
[%]
BTp 0th ARC
0.03
-26-12.9
BTp 1st ARC
0.102
2.5
Slope 1
-
-
BTp 2nd, 3rd ARC
-
-
Slope 2
-
-
BTp 4th ARC
-
-
e;
<!x2>1/2 [m] <!y2>1/2 [m]
Fudge Factor of Quadrupole
Correction
Before After Before
0.13 0.11 0.05
0.11 0.02 0.01
0.102 0.038 0.029
0.066 0.029 0.037
0.104 0.091 0.192
- - -
After
[%]
Slope 1
0.01
1.0-5.9
Bte 0th ARC
0.02
0-6.7
Bte 1st ARC
0.036
2.37
Bte 2nd, 3rd ARC
0.034
2.52
Slope 2
0.116
3.55
correction for e- and Bte 4th ARC
-
-
BT-WS placed
BT-WS placed
Until BT-Wire Scanner (WS) position, dispersion correction was done.
In some ARC, dispersion correction is not finished. → Continue to Phase-III
Inj. point to MR
Inj. point to MR
As a same manner, we corrected dispersion in each ARC of BT.
This table shows residual dispersion before and after
e+ beam.
These ARC names are listed from the upstream of the beam line.

## Slide 42: B) Beam Phase Space Jitter (2)
First, we suspected that components around the target made beam jitter.
They are flux concentrator, solenoid, bridge coil, pulsed magnet, chicane, and so on.
We check whether these components are sources of jitter or not by turn off these components.
There is not remarkable differences.
The components are not the beam jitter source.

## Slide 43
D) Emittance growth induced by radiation excitation in BT
Theoretical emittance growth induced by radiation excitation:
∝ !5, 1/$3
Particle tracking simulation was performed from the end of LINAC to the end of BT.
Initial horizontal emittance of e8 and e+ beam have 20 and 64 µm, respectively.
These emittances are increased by radiation excitation and reach 68 and 74 µm.
Even if the emittance preservation is perfect in the LINAC, emittance growth by radiation
excitation is larger than Phase8III final requirement for the e8 beam.
We seek a solution of this problem now. One possible way is that other tunnel (AR line) is used as
e8 beam line, which has smaller ρ than that of current beam line.
N. Iida | Initial particles |  | With Radiation | Phase2III3final requirement
 | e8 (7 GeV) !" x [µm] | 20 | 68 | 40
 | e+ (4 GeV) !" x [µm] | 64 | 74 | 100

## Slide 44: Emittance measurement (e.)
N. Iida
Left and right figure show horizontal and vertical emittance measured at each sector, respectively.
Green and blue plot show emittance of beam generated by RF gun.
Manual orbit correction was done so as to reduce the orbit distortion. By this correction,
emittance was reduced.
In Phase.II, the requirement of e. emittance at the end of LINAC was satisfied.
However, emittance was increased in BT though dispersion correction was done.
This growth is not caused by radiation excitation because BT.WS is placed around the start of BT.
X
Y
1.2nC
Phase.III
Phase.III
Phase.II
Phase.II
reduced by orbit correction
5 BT
B C
5 BT
B C

## Slide 45: Emittance measurement (e+)
In Phase3II, the requirement of e+ emittance at the end of LINAC was also satisfied.
However, e+ emittance was also increased in BT though dispersion correction was done.
Investigations for this emittance growth source in BT are under going.
0.7nC
Y
B C
5 BT
B C
5 BT
X
Phase3II
Phase3III
Phase3III
Phase3II
N. Iida

## Slide 46: Klystron Modulator Installation and Temporary Gun Removal
KL_DS/BCS
KL_DN/ECS
KL_32
 | ECS | BCS
Voltage required [MV] | 41 | 21.5
# 2m accelerator structure | 2 | 1
Accelerator field [MV/m] | 10.2 | 10.75
Operation power [MW] | 29.0 | 19.0
Pulse width [µs] | 0.8 | 0.8
Rep. rate [Hz] | 50 | 50
Other Improvements

## Slide 47: Examples of Other Recent Improvements
Energy and bunch compressors on the beam transport of DR
Beam lines and power supply rearrangement for DR BT
Thermionic gun and bunchers
Beam position monitors
Wire scanners and streak cameras
LLRF system to co-op with event timing controls
LLRF monitors
Independent RF amplifiers
Alignment
Direct beam transport to PF-AR
Safety system and radiation control licenses
Rejuvenation of old components
Operation software
Operation manuals
Other Improvements