## Slide 1: Injector challenges
2020.2.10
M. Satoh (KEK, Acc. Lab.)
for Injector Linac Group
14th annual Belle PAC Review meeting, Feb. 10-12, 2020

## Slide 2: Contents
Injector operation status
e- and e+ beam sources
Accelerating structures
Beam controls
  Energy and orbit feedback loops
  Dispersion correction
  Emittance
Summary and plan

## Slide 3: Linac Beam Parameters for KEKB/SuperKEKB
Stage | KEKB (final) |  | Phase-I |  | Phase-II |  | Phase-III (interim) |  | Phase-III (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1.0 A | 1.0 A | – | – | 1.8 A | 1.3 A | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | – | – | 6 | 6
 | primary e- 10 |  | primary e- 8 | 1 | 0.5 | 1 | 2 | 2 | primary e- 10 | 4
Bunch charge (nC) | → 1 | 1 | → 0.4 |  |  |  |  |  | → 4 | 
Norm. Emittance | 1400 | 310 | 1000 | 130 | 200/40 | 150 | 150/30 | 100/40 | 100/15 | 40/20
(gbe) (mmrad) |  |  |  |  | (Hor./Ver.) |  | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.)
Energy spread | 0.13% | 0.13% | 0.50% | 0.50% | 0.16% | 0.10% | 0.16% | 0.10% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Partially |  | 4+1 rings (LER, HER, DR, PF, PF-AR) |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 

## Slide 4: Injector overview
2
1
C
3
4
5
Low emittance RF e- gun
Thermionic DC e- gun
SectorA
B
1.5 GeV
e+ target
e-:Chicane
1.1 GeV
e+DR
Decelerate
e+ target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
same energy
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
or 5 GeV
PF: 2.5 GeV e-
LER: 4 GeV e+
Photocathode RF gun for HER injection
Thermionic gun for LER, PF, PF-AR
Pulsed quads, steering magnets
Notes: RF電子銃でHER入射を，それ以外のリングには熱電子銃が使用されている．
下図は，入射器全景と各ビームモードのエネルギー変化（場所ごとの）を示している．
PFなどの低エネルギービームも前半はなるべく加速し，共通オプティクス部分を確保している．（上流部はDC電磁石が主であるため．）
Jアーク部のエネルギーは，被災により1.5 GeVから1.35 GeVに変更になっている．

## Slide 5
Pulse to pulse switching: rf e- gun/thermionic e- gun
Thermionic DC e- gun (GU_AT)
w/ 2 subharmonic bunchers and 2 bunchers
・e+ production e-: 10 nC (for LER injection)
・e- study/HER injection: 1 nC
・PF injection: 0.3 nC
・PF-AR injection: 0.3 nC
RF e- gun
（GR_A1 for HER injection）
Pulsed bend rep. up to 25 Hz (LER + PF + PF-AR)
(magnet coil and chamber heating issue)
It will be replaced by new one in summer shutdown 2020.
Notes: 入射部では24度垂直偏向パルスベンドを用いて，熱電子銃，RF電子銃を切り替えて運転している．
熱電子銃は，陽電子生成用10 nC電子ビーム，PF,PF-AR入射用 0.3 nCビームを生成している．
RF電子銃は，HER入射用低エミッタンス電子ビームを生成している．（レーザー両打ち，IrCeカソード）電子銃からは，最大2～3 nC出る．

## Slide 6: Simultaneous beam operation (w/ thermionic and rf e- gun)
Hor. orbit
Ver. orbit
Bunch charge
Hor. orbit
Ver. orbit
Bunch charge
rf gun
Thermionic gun
Thermionic gun
Thermionic gun and damping ring
Stable simultaneous top up injection to 4 storage rings (HER, LER, PF, and PF-AR) w/ thermionic gun, rf gun, pulsed magnets.

## Slide 7: Simultaneous Top-up Injections
SuperKEKB integrated luminosity improvement
17.5 /pb in 5.15 hr
(5 fills)
on May. 6
41.6 /pb in 5.15 hr
(top-up)
on May. 16
237% improvement

## Slide 8: RF e- gun
M. Yoshida, SuperKEKB review, Mar. 14th, 2018
Low emittance
rf gun
Photocathode
(metal composite: IrCe)
QTW RF gun or operation (0 deg. Line)
CDS RF gun
for backup (90 deg. Line)
Yb-doped-fiber and Nd/Yb:YAG laser
IrCe cathode
QTWSC or cut disk cavities

## Slide 9: HER injection beam (rf e- gun) status
HER injection has been done w/ only rf gun from PhaseIII day 1. (Mar. 11th , 2019)
Laser system has no significant fault.
In summer shutdown of 2019, photocathode (Ir7Ce2) was replaced by new one (Ir2Ce) for aiming at better quantum efficiency (Qe).
  Discharge, frequent VSWR, gradual decrease of bunch charge
In this winter shutdown,
  Even after applying thermal cleaning of cathode, bunch charge is not stable.
  Finally, photocathode was replaced by previous one (Ir7Ce2) toward next run. Now, under rf conditioning.

## Slide 10
Ir7Ce2
2019

## Slide 11: Qe of photocathode (Ir7Ce2, Ir2Ce)
M. Yoshida

## Slide 12
discharge
discharge
VSWR
VSWR
VSWR
VSWR
VSWR
Ir2Ce
2019

## Slide 13
Laser
cleaning
M. Yoshida, B2GM, Feb. 6th, 2020
Thermal
cleaning

## Slide 14
M. Yoshida, B2GM, Feb. 6th, 2020
Before laser cleaning
Laser cleaning ～ 30 min.

## Slide 15: e+ source setup 1
Positron target and capture section
Y. Enomoto, SuperKEKB review, 2019
W target + flux concentrator (FC)
DC solenoid
Large aperture S-band acc. Structures (x10)

## Slide 16: Pulse to pulse e-/e+ beam switching
Pulsed steering magnet control e- beam orbit．
Low emittance e- beam goes through a hole at center of beam line.
hole (F2 mm)
for low emittance e- beam
W target (F4 mm)

## Slide 17
Primary
e- beam
e+ beam
e+ beam history in 2019
2019

## Slide 18: LER injection beam status
Bunch charge
  Stable and enough bunch charge in this stage
  Primary e-: 11 nC (from gun), 9 nC (on W target), e+ : 1.2 nC (linac end), 0.8 nC (BT)
Flux concentrator (FC)
  Previous FC was damaged by large discharge during PhaseII. It was removed in Sept. 2018.
  Current FC was installed in Jan. 2019.
  2 ～ 3 kA operation current (design 12 kA) for stable operation. no significant fault.
  New FC made of Cu-alloy (NC50: Cu-Si-Ni) has been tested w/o fault (～ 12 kA).
  New FC will be installed in summer shutdown of 2020 for aiming at design operation current.
Requirements for material of the FC head are
Good brazing characteristic
High yield strength even after brazing
High electric and thermal conductivity

## Slide 19: After large discharge…
After large discharge
Slit gap got narrow.
Not possible to apply high voltage unless the gap will be expanded.
Y. Enomoto, SuperKEKB review, 2019

## Slide 20: Accelerating structures
Approx. 230 accelerating structures employed
Many aged (40 years-old) structures are degraded
  Risk of 7 GeV / 4 GeV acceleration for Y(4S)
  Cannot reach Y(6S)
As a 4-5 year plan, structures are being fabricated since the last year
First tests will be performed at the assembly room
Possibly, a couple of structures would be installed during summer

## Slide 21: Feedback loops
Energy feedback (J-ARC, LTR, ECS, BT) work fine.
  Energy stability at BT line < 0.025%
Orbit feedback at some locations.
  Large drift (～ 1 mm) can be corrected
  within ~ 0.1 mm w/ feedback.
Energy @ BT
Orbit FB
Energy FB

## Slide 22: Dispersion measurement and correction
Design
J-ARC
chicane
Before correction
Measured
After correction
Disp. correction
w/ quads
Horizontal dispersion leakage from J-ARC causes the beam position jitter.
Applying fudge factors to quads in J-ARC, dispersion is well corrected.
Y. Seimiya

## Slide 23: Residual Dispersion in the BT line
BT for e+
BT for e-
The dispersion functions have been corrected for each BT ARC one by one.
Non-negligible residual dispersion is still observed
Straight line
(BT2)
Straight line
(BT2)
Straight line
(BT1)
Straight line
(BT1)
Y. Seimiya

## Slide 24: Vertical emittance vs. HER Injection efficiency
Y. Ohnishi
Injection efficiency and background

## Slide 25
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
Y. Ohnishi
・LER
(28/Jun/2019)
(6/Nov/2019)
gex
[mm]
gey
[mm]
Reducing emittance is in time for by*=1mm
Injection efficiency and background
e+ horizontal emittance has been improved after ECS bend alignment.

## Slide 26
N. Iida, SuperKEKB workshop, 2019

## Slide 27
Measured emittance
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
e+ beam (Phase3.2(6.Nov.2019))
Emittances increase
DR → Sector3
BT1 → BT2
Beam study will be continued
Phase3.3 | e+ | e-
gex [mm] | 150 | 100
gey [mm] | 30 | 40
sd [%] | 0.16(1s) | 0.1(1s)
e- beam (Phase3.2(4.Dec.2019))
B C ３ 5 BT1 BT2
B C ３ 5 BT1 BT2
Emittances increase
C→Sector3
BT1→BT2
Beam study will be continued
gex
[mm]
gey
[mm]
gex
[mm]
gey
[mm]

## Slide 28: Fast beam position monitor(BPM) in LINAC
1. Jun., 2019 19:56
  LER D6V2 LM abort
Y. Seimiya, F. Miyahara, T. Miura, Y. Enomoto, H. Kaji et al.
No energy deviation
Orbit deviation
Dispersive point
Straight line
One station for the power supplies (PS) was set to 0 [A] due to a trigger missing of the PS.
The klystron 51 was down at the time.
The estimation was -46.5 MeV which is consistent with the beam position.
Beam energy was 50 MeV lower.
Injection beam just before abort can be monitored by,
1. Jun., 2019 21:19
  LER D6V2 LM abort
Dispersive point
Straight line
Beam abort caused by abnormal injection beam

## Slide 29: Summary and plan
Stable simultaneous top up injection to 4 storage rings (HER, LER, PF, and PF-AR) w/ thermionic gun, rf gun, pulsed magnets.
HER injection has been done w/ only rf gun from PhaseIII day 1.
  Laser system has no significant fault.
  Photocathode: Ir7Ce2 => Ir2Ce (summer of 2019) for higher Qe, however, bunch charge gradually decreased.
  In this winter shutdown: back to Ir7Ce2 photocathode
  Laser cleaning can cure degradation of Qe
Flux concentrator for e+ beam has no significant fault.
  New flux concentrator will be installed for higher e+ bunch charge for higher e+ bunch charge.

## Slide 30: Summary and plan (cont’d)
Smaller emittance, higher injection efficiency, smaller background.
Emittance growth (need more beam study)
  btwn BT1 - BT2 (e-, e+)
  DR – Sector3 (RTL) (e+), SectorC-Sector3 (e-)
  Steering magnets and BPMs will be installed in e+ capture section (solenoid section) at Sector1.
  Movable girder and precise orbit control will help for emittance preservation.
Single shot beam w/ bad quality (energy, orbit) could cause abort.
  Install collimator at ECS (end of linac) in this summer shutdown.
  Reduce failure rate of PS control software

## Slide 31: Backup

## Slide 32: Fire recovery
Fire at acc. structure assembly room on Apr. 3, 2019
  Southern part of the injector was much damaged as well as the assembly room
Interim injector recovery by Apr. 26, 2019
Full injector recovery during summer shutdown
The assembly room cleaned up
  Restoration in April
  S-band structure tests and RF conditioning soon
Scaffold to clean up walls and ceiling
at acc. structure assembly room

## Slide 33: Beam emittance example (~1 nC) w/ multiple wire scanners
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
e+: ex/ey ～100/6 mm
e-: ex,y ～20 mm
e-: ex,y ～ 50～80 mm
e+: ex/ey ～100/2 mm
e-: ex/ey 40/20 mm
e+: ex/ey 100/15 mm
BT
#1 straight
Final target (4 nC)
e-: ex,y ～ 50～80 mm
e-: ex,y ～10~20 mm
e- emittance growth
e+: ex,y ～ 2500 mm (before DR)
Notes: 1 nCでのエミッタンス測定の典型的な例（4台のワイヤースキャナで測定）
Phase3の最終目標は，4 nCで中央下にある値．
1nCであるが，陽電子は，概ね最終目標エミッタンスを満たしている．
電子も1nCであるが，入射器内（5セクタ）では水平方向は50 um程度の場合もある．C～5セクタでのエミッタンス増大は，アライメントの改善と加速管架台ムーバーの導入で改善を図る予定である．
Phase2の時には，BTでエミッタンス増大が見られる（入射器5セクタの2～3倍のエミッタンスになる．100 um が300 um以上になる）問題があったが，BTワイヤスキャナのワイヤ径を200 umから60 umに変更し，データ収集系をCAMACから入射器と同じVMEベースのものに変更したところ，そのような増大が見られなくなった．（詳しい原因は不明ですが，測定系に問題があったと思われます．）

## Slide 34
PF injector
Tristan
KEKB
SuperKEKB

## Slide 35: e+ vertical emittance was improved
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
6.Nov.2019 3:17
6.Nov.2019 18:50
BG due to injection became smaller.
Signals from Loss monitors in the LER
BGs from Vertex detectors
gex
[mm]
gey
[mm]
LER
Injection efficiency and background

## Slide 36: Monitors
Beam position monitor (x 103)
  Four strip line electrodes (x 97)
    Measurement precision ~ 10 mm
  Eight strip line electrodes (x 6) (J-ARC, LTR x2, PF BT, HER BT, LER BT)
Profile monitor (x 104)
  Al2O3/CrO3 (AF995R, Demarquest Co.). (t: 1 mm, 0.1 mm), YAG:Ce (t: 0.1 mm)
Wire scanner (WS) (x 6)
  SectorA, B, C, 2, 3, 5
Streak camera (ST) (x 2)
  SectorA, C, 3
RF monitors for klystron, SLED, acc. structure
WS
WS
WS
WS
WS
ST
ST
ST
WS

## Slide 37: Pulsed magnet system
Pulsed quads (x 28) (w/ ceramic duct) and steering (x 36) were installed at Sector3 to Sector5 in 2017 (on movable girder).
Pulsed bend, additional quad and steering were installed in 2018 summer and winter shutdown.
PXIe based control system (Windows 8.1, LabVIEW, EPICS) have worked fine w/o any serious trouble.
Power supply stability: 0.01% (24 hours)
Pulsed magnet
BPM
Movable girder for pulsed magnet
(remote controllable, 10 mm step)

## Slide 38: e+ source setup 2
target
BC (bridge coil)
FC(flux concentrator) head
LAS (large aperture S-band)
solenoid
FC head + BC + target = FC assembly
Y. Enomoto, SuperKEKB review, 2019

## Slide 39: Movable girder for accelerating structure
Six movable girders have been installed in Sector3 (in summer shutdown of 2019).
  Four 2-m-long accelerating structures are mounted on one girder.
It could help to suppress emittance growth due to misalignment.

## Slide 40
2020
Ir2Ce
One day