## Slide 1: Progress of KEK Electron/Positron Injector Linac
Mitsuhiro Yoshida
Injector Linac, KEK

## Slide 2: Mission of Electron/positron Injector in SuperKEKB
  For 40-times higher luminosity in SuperKEKB collider
  Low emittance & low energy spread injection beam with 4-5 times more beam current
    New high-current photo-cathode RF gun
    New positron capture section
    Damping ring construction
    Optimized beam optics and correction
    Precise beam orbit control with long-baseline alignment
    Simultaneous top-up injection to DR/HER/LER/PF/PFAR
  Balanced injection for the both photon science and elementary particle physics experiments
Injector Linac Mission
The single injector would behave as multiple injectors to multiple storage rings by the concept of virtual accelerator
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: Required injector beam parameters
Stage | KEKB (final) |  | Phase-I |  | Phase-II |  | SuperKEKB (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1 A | 1 A | – | – | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | 6 | 6
Bunch charge (nC) | primary e- 10 → 1 | 1 | primary e- 8 → 0.4 | 1 | 0.5 | 1 | primary e- 10 → 4 | 4
Norm. Emittance (ge) (mrad) | 1400 | 310 | 1000 | 130 | 200/40 (Hor./Ver.) | 150 | 100/15 (Hor./Ver.) | 40/20 (Hor./Ver.)
Energy spread | 0.125% | 0.125% | 0.5% | 0.5% | 0.16% | 0.1% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 / 50 Hz |  | 25 / 50 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Eventually |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 

## Slide 4: Linac Schedule Overview as of Jun.2017
: Electron
: Positron
: Low current electron
2 nC
Phase2
1 nC
Phase1
Location
↓
Time →
Schedule
Without Top-up
4 nC
Phase3
Direct PF-AR BT
DR Commiss.
Beam Licenses in steps
Low Emittance Beams
4+1 Ring
Injections
Long (5-month) shutdown for the first time in SuperKEKB project
  9-month shutdown in 1997 during KEKB
  DR construction, resource availability, etc
  Installation of many important components during this shutdown

## Slide 5: Progress of Photo-cathode RF Gun
Photo-cathode RF Gun
Yoshida et al
Thermionic gun
Primary RF gun
New secondary RF gun
Beam orbit measurement
IrCe Cathode
Succeeded in injection during SuperKEKB Phase-1 commissioning for 11 days
Employs Yb-doped-fiber and Nd/Yb:YAG laser, Ir5Ce or Ir2Ce cathode, QTWSC or cutdisk structures
Secondary RF gun was constructed for availability with Ir2Ce and cutdisk
Cutdisk cavity

## Slide 6: Photo-cathode RF gun: Laser
Yb:Fiber + Nd:YAG multi-pass amplifier
Beam charge stability
1.57 +/-0.032 nC
E.O.
Fiber Amp
Nd.YAG Φ2mm
×2pass
Nd.YAG Φ4mm
×8pass
~30 μJ
Pockels Cell
Nd.YAG Φ4mm
×4pass
~700 μJ
SHG
FHG
2 mJ
1.0 mJ
200 μJ
Nd.YAG Φ4mm
Stable laser system for Phase-II.
  2 nC, 2 bunch stable operation will be expected. (2-bunch operation was already demonstrated.)
  Two oscilllator (one will be commercial oscillator).
  Two amplifier lines.
  Spatial filter for one amplifier line.

## Slide 7: Removal of temporary pre-injector (3T/32RFgun)
KEK e+/e- linac has been divided into two regions by a wall at 3T.
3T/32 pre-injector has been used for PF, AR injection during upgrade construction and initial beam commissioning in linac upstream region.
3T/32 pre-injector is removed in May 2017 for DR commissioning.
a regular accelerator module (3-2) is installed in this region for injection beam energy margin.
AT/A1 pre-injector is used for all the storage rings (HER, LER, PF, AR) after autumn 2017. They share the same fate in case of linac troubles.
PF, AR beam operation from October.
DR commissioning from December 2017.
wall
3T pre-injector
32 pre-injector
After the wall and
3T/32 pre-injector
removal, linac tunnel
is united as one.

## Slide 8: Positron Source status
Breakdown problem in Flux Concentrator during 2017 April operation after beamline installation (Though we had no problem during test-stand operation at full-spec current.)
No e+ beam operation during April-May run.
Inspection of damaged FC
  cooling down of residual-radiation since May 15
  removal of FC base part from e+ station in June
  visual search for damaged part
  detailed inspection in August
  recovery trial
Re-installation or replacement to spare FC in August for 2017 autumn run & Phase-2 run. (During these period, operation current will be around half of the spec.)
Manufacturing of next FC assembly on-going for stand-alone test and investigation of the breakdown issue for Phase-3 operation.
return
yoke
Flux
Concentrator
Target

## Slide 9: Pulse magnet system
For pulse-by-pulse beam-mode switching and independent optics/orbit tuning, pulse magnet system is introduced.
All the quads in Sector-3, 4, 5 are replaced by pulse-Qs and pulse-steerings are introduced.
AT/A1 pre-injector merger line bends are replaced from DC to pulse magnets.
Pulse magnets installation completed.
Pulse power supply setting-up on-going.
Test operation of pulse magnet system in September.
Beam commissioning with pulse magnet system start in October 2017.
Pulse current driver
Pulse magnets (Q+ST+ST+Q)

## Slide 10: Event timing controls for pulsed quad & steering magnet controls
MRF PXI-EVR-230 was added
Control software is based on:
Windows 8.1 Professional
EPICS base R3.14.12.6 for EVR control
LabView for DAC/ADC control
Device driver for cPCI-EVR-300 (Swiss FEL) was modified for our card
Fundamental functions can already work well.
Data buffer functionality is now under implementation.
Satoh, Enomoto et al.

## Slide 11: Pulsed magnet rack
Remote controller
DAC (PXI-6733)
ADC (PXIe-6356)
PXI-EVR-230
PXI chassis
(PXIe-1082)
Edge switch
Interlock signal processing
(CompactRIO based system)
Control
PC
Pulsed magnet driver
DC Power Supplies
13 racks are newly installed
Small form-factor (4U) power supplies are tested more than 2 months at 50Hz

## Slide 12
φ2 changed at 50 Hz
All linac clocks are generated from 571.2 MHz master oscillator
Clock is adjusted every minutes to compensate the ring circumferences, and the phase should be adjusted to meet the lengths of beam transports of electron and positron.
Stabilities of 0.1%rms in amplitude and 0.02 degree rms in phase
Development of 571.2MHz Master phase shifter
3,4,5セクター
2856MHz移相器

## Slide 13
571.2MHz
571.2MHz Phase shifter

## Slide 14: KL_DS, KL_DN , KL_32 Installation
KL_DS/BCS
KL_DN/ECS
KL_32
 | ECS | BCS
Voltage required [MV] | 41 | 21.5
# 2m accelerator structure | 2 | 1
Accelerator field [MV/m] | 10.2 | 10.75
Operation power [MW] | 29.0 | 19.0
Pulse width [µs] | 0.8 | 0.8
Rep. rate [Hz] | 50 | 50

## Slide 15: Bucket selection in Phase-2 with DR
Without DR, simply wait up to 5120 x 96 ns ~ 490 μs
  96 ns : highest common frequency between linac – ring
With DR, in order to select arbitrary bucket in MR, have to wait up to ~4.5 ms, even if a bucket in DR was carefully selected
  Power supply can wait only 2 ms, one of only 2798 buckets in 5120 buckets can be selected, may have to change LLRF condition at latter half of linac every pulse
  Can be a big challenge in LLRF precision
ARC
e+ Target
e+ BT (3.5GeV, 0.6nC)
e− Gun
KEKB
Primary e– (3.5GeV, 10nC)
ARC
e+ Target
e+ BT (KEKB: 4GeV, 4nC)
e− Gun
SuperKEKB
Primary e– (3.5GeV, 10nC)
e+ DR (1.1 GeV, 4nC)
96ns
>100ns
>100ns
96ns
Kaji et al

## Slide 16: Many other Linac Upgrade Progress
High-power microwave modulator upgrades
Low-level RF controls/monitor upgrades
  Pulse-to-pulse modulation (PPM) between 4+1 rings
  More spaces for increasing number of devices
Beam instrumentation
  Large/small aperture beam position monitors (BPM)
  Precise/fast and synchronized BPM readout system
  Wire scanners and beam loss monitors
  Streak cameras
  (Deflectors, etc.)
Alignment to preserve beam emittance
  Measurement precision reaching 0.1 ~ 0.3mm
  Mover and orbit control development
Event-based control and timing upgrade
  Essential for pulse-to-pulse modulation
  Precise timing & synchronized controls
  Bucket selection at DR and MR
SINAP event modules
Linac Upgrade Overview
Beam wire scanner
Pulse magnet tests

## Slide 17: Linac Schedule Overview as of Jun.2017
RF-Gun e- beam
commissioning
at A,B-sector
e- commiss.
at A,B,J,C,1
e+ commiss.
at 1,2 sector (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 sector
non damped e+ commiss.
at 1,2, 3,4,5 sectors
e- commiss. at A→5 sectors
damped e+ commiss.
at 1→5 Qe+ = 1~4nC
e- commiss.
at A→5 Qe- = 1~5nC
: Electron
: Positron
: Low current electron
2 nC
Phase2
1 nC
Phase1
Location
↓
Time →
Phase1: high emittance beam for vacuum scrub
Phase2,3: low emittance beam for collision
New Schedule
Without Top-up
4 nC
Phase3
Improved RF gun
Direct PF-AR BT
DR Commiss.
Beam Licenses in steps
Low Emittance Beams
4+1 Ring
Injections

## Slide 18: Summary
We learned a lot during KEKB operation
Phase-2 injection into SuperKEKB is another challenge with higher beam current and lower transverse and longitudinal emittance
Steady progress towards designed injection beam in steps
  Alignment: almost confident on the measurement precision (0.1-mm local, 0.3-mm global), may need mover to maintain it for longer term
  Positron generator: need discharge analysis
  Thermionic gun: stably operated for primary electron for positron generation
  RF gun: following recommendations at review meetings
  Pulsed devices: global and synchronized operation
  New modulators for energy and bunch compressors on DR beamlines
Will balance between final beam quality and progressive operation
Will select optimized route depending on available resources
  Balance with injection operation for light sources, commissioing and development in parallel
Summary

## Slide 19: Injection Energy Margin Recovery (even while dropping Energy 8 GeV  7 GeV)
No backup/stand-by before J-Arc in KEKB operation
Optimized for SuperKEKB ring injection reliability with larger beam currents and smaller emittance
Temporary removal of units for construction
  Should be recovered before phase-3
A unit was removed to make a room for DR BT
Positron deceleration capturing
Lower acceleration in large aperture structures in the positron capture section
An unit before J-Arc was converted into a stand-by for availability
C-band structures were converted into S-band to help emittance preservation
Degraded accelerating structures after 35 years of operation
  Should be refurbished in the long run
Larger beam current with larger beam loading
Kamitani et al